- Simon Chen
Intro To OS
Homework 2
Spring 2017

1)

the $ prefix is for immidiates (constants), and the % prefix is for registers (they are required*).
   [f000:fff0] 0xffff0:	ljmp $0xf000,$0xe05b

   0xfe05b:	cmpl $0x0,%cs:0x6574
   Compare check if the value at x6574 is 0

   0xfe062:	jne 0xfd2b6
   jump into fd2b6 if value at x6574 is not 0;
Since next memeory locaiton is still fe066, it didn't jump

   0xfe066:	xor %ax,%ax
Checks if %ax, %ax are different
They are the same thing, so the xor returns a false

   0xfe068:	mov %ax,%ss
mov %ss into %ax
Moves the value at ss (segment register) into the register ax

Skipped because the previous condition was false

   0xfe06a:	mov $0x7000,%esp
move %esp into $0x70000
Moves value in %esp(stack pointer) into 0x7000

   0xfe070:	mov $0xf3c24,%edx
move %edx into $0xf3c24
Moves value in %edx(data) into 0xf3c24

   0xfe076:	jmp 0xfd124
jump into fd124

Assumed unconditional control jump transfer; so the next control transfer instruction

2)
At what point does the processor start executing 32-bit code? What exactly causes the switch from 16 to 32-bit mode?

It transitions from executing 16-bit code to 32-bit when it performs mov &cr0,& eax

What is the last instruction of the boot loader executed, and what is the first instruction of the kernel it just loaded?

The last instruction of the boot loader is 0x7d61: call 0x10018. The first instruction from the kernet is movw $0x1234,0x472.

How does the boot loader decide how many sectors it must read in order to fetch the entire kernel from disk? Where does it find this information?

It depends the sectors by reading into the kernel file. It starts at 0x10000c and reads into the kernel's first 8; so 8 sectors.	The kernel has an ELF header at the boot loader uses to read.

EIP & CS
ljmp $0xf000,$0xe05b
eip 0xfff0	0xfff0
cs 0xf000	61440

0xfe05b:	cmpl $0x0,%cs:0x6574
eip 0xe05b	0xe05b
cs 0xf000	61440
3)

Assume int a[4] is stored at memory location 0x40000 first
void
f(void)
{
    int a[4];
    int *b = malloc(16);
    int *c;
    int i;

    printf("1: a = %p, b = %p, c = %p\n", a, b, c);

    c = a;
    for (i = 0; i < 4; i++)
  a[i] = 100 + i;
    c[0] = 200;
    printf("2: a[0] = %d, a[1] = %d, a[2] = %d, a[3] = %d\n",
  a[0], a[1], a[2], a[3]);

    c[1] = 300;
    *(c + 2) = 301;
    3[c] = 302;
    printf("3: a[0] = %d, a[1] = %d, a[2] = %d, a[3] = %d\n",
  a[0], a[1], a[2], a[3]);

    c = c + 1;
    *c = 400;
    printf("4: a[0] = %d, a[1] = %d, a[2] = %d, a[3] = %d\n",
  a[0], a[1], a[2], a[3]);

    c = (int *) ((char *) c + 1);
    *c = 500;

f:
Instruction | Mem. Location |

4)
The kernel starts at 0xf0100000 which is passed to the readseg function. It turns into 0xFFFFFF, because it loads the kernel text program. The first 8 words contains the first 8 words of the kernel program. The second break point is because of the newer computer architecture. It'll need to switch from old to new.